## Slide 1: Motion Transmission Systems

## Slide 2: Motion Transmission
A) Definition:
    Relaying the same type of motion from one part of an object to another (rotational to rotational, translational to translational)
  Motion transmission systems contain:
      A driver component that initiates the motion
      At least a driven component that receive the motion and transfers it
      Might contain Intermediate components between the driver and driven components

## Slide 3: Motion Transmission
B) Types of motion transmission systems
  Gear Train
  Chain and Sprocket

## Slide 4: Motion Transmission
B) Types of motion transmission systems
3. Worm and Worm Gear
4. Friction Gear Systems

## Slide 5: Motion Transmission
B) Types of motion transmission systems
5. Belt and Pulley System

## Slide 6: Motion Transmission
B) Types of motion transmission systems
Gear Trains
Chain and Sprocket
Worm and Worm Gear
Friction Gear System
Belt and Pulley

## Slide 7: Motion Transmission
1. Gear trains
Contains at least two gears that meet and mesh together
Direction of components | Alternates from one gear to another
Reversibility | Yes

## Slide 8: Motion Transmission
When building a gear train, you must consider:
1. The Gear teeth
(they must be evenly spaced, the same size and have the same direction)
2. The Gear types
(straight gears vs. bevel gears)
3. The Gear size
higher number of teeth = slower rotation
larger diameter = slower rotation

## Slide 9: Gear Types
Straight Gear (a.k.a Spur Gear)
Gears are right next to each other (at 180 degree angle)
Bevel Gear
Gears meet at 90 degree angle

## Slide 10: Motion Transmission
When building a gear train, you must consider:
1. The Gear teeth
(they must be evenly spaced, the same size and have the same direction)
2. The Gear types
(straight gears vs. bevel gears)
3. The Gear size
higher number of teeth = slower rotation
larger diameter = slower rotation

## Slide 11: Motion Transmission
2. Chain and sprocket
Connects components that are far away from one another.
The gears (sprockets) do not mesh together; they are connected with a chain
Direction of components | The sprockets inside the chain will turn in the same direction.
Reversibility | Yes

## Slide 12: Motion Transmission
When building a chain and sprocket, you must consider that:
    The teeth on the sprocket are identical
    The chain links must mesh easily with the sprocket’s teeth
    The system requires constant lubrification
    The smaller the sprocket the faster it turns

## Slide 13: Motion Transmission
3. Worm and worm gear
  Consists of one endless screw and at least a gear
  It is not reversible
  When building a worm and screw gear, you must ensure that:
  The gear teeth match the worm’s grooves
  The driver must be the worm

## Slide 14: Motion Transmission
4. Friction gear systems
  Similar to gear trains yet less efficient because the friction gears can slip.
  The teeth on gear trains “lock” the gears in place to prevent slipping; there is no such thing in Friction gear systems
  The larger the gear the slower the rotation

## Slide 15: Motion Transmission
5. Belt and pulley system
  When building a belt and pulley system, you must ensure:
    Pulleys must contain a groove where the belt can fit
    The belt must adhere (stick) to the pulleys
    The smaller the pulley the faster it turns

## Slide 16: Speed Change
In Motion Transmission Systems

## Slide 17: Speed Change
1. Worm and worm gear
For each turn of the worm, the gear moves by one tooth.
The greater the number of teeth the slower the speed.

## Slide 18: Speed Change
2. Remaining systems
The speed varies with the number of teeth (or the diameter of the gears)
  If motion is transmitted to a smaller gear, the speed is increased
  If motion is transmitted to a larger gear, speed is decreased
  If motion is transmitted to a gear of equal size, there is no speed change

## Slide 19: Speed Change
To find out the exact speed of the driven gear we must find the speed ratio:
Speed ratio = diameter (or # of teeth) of the driver gear
  diameter (or # of teeth) of the driven gear
What does this mean exactly?
    If I have a driver gear with 20 teeth and a driven gear with 10 teeth. The speed ratio is 2.
      This means that the driven gear is turning twice (2 x) as fast of the driver gear.

## Slide 21: Motion Transformation systems

## Slide 22: Motion Transformation
A) Definition
    Relaying a motion from one part to another while altering the nature of the motion (e.g. rotation to translation or translation to rotation)
B) Types of motion Transformation systems
    Rack and pinion
    Screw Gear systems
    Cam and follower
    Slider–Crank mechanism

## Slide 23: Motion Transformation
1. Rack and Pinion
  Contains a rack (straight bar with teeth) and a pinion (gear)
While building a rack and pinion you must ensure that:
  The teeth on the rack and on the pinion must be identical
  The system requires frequent lubrification
  The greater the number of teeth on the pinion the slower the rotation

## Slide 24: Rack and Pinion uses
Steering wheels for cars

## Slide 25: Motion Transformation
2. Screw gear systems (2 Types)
  Contains a screw and a nut
  Type 1: the screw is the driver
    Transforms rotational motion into translational motion (e.g. jack to lift the car)
  Type 2: the nut is the driver
    Transforms rotational motion into translational motion (e.g. wrench)

## Slide 26: Screw Gear Systems uses
Type one: Car Jack
The Screw is turned, which allows for translational motion of the jack to rise

## Slide 27: Screw Gear Systems uses
Type Two: Wrench
It’s the nut that does the initial rotational movement

## Slide 28: Motion Transformation
3) Cam and Follower
  Rotational motion changed to translation motion
When building a cam and follower, you must ensure that:
  The follower must be guided in its translational motion
  The shape of the cam determines how the follower will move
  A device such as a return spring is usually necessary to keep the follower in continual contact with the cam.

## Slide 29: Cam and Follower Uses
Toys

## Slide 30: Cam and Follower Uses
Water Powered Mill
The water falling down the wheel creates rotational motion, this wheel is connected to an bar, which is connected to a cam and follower. The follower has a stamping-battery at the end which pounds on the ore

## Slide 31: Motion Transmission
4. Slider-crank mechanism
  This is the mechanisms used in pistons

## Slide 32: Slider-Crank Uses
Trains-wheels

## Slide 33: Slider-Crank Uses
Internal Combustion Engines-Cars